## Slide 1
Cover Glass Manufacturing Quality Analytics
Simulated MQE / Brittles portfolio project
Synthetic data only
Hexing Yin
Ph.D. in Materials Science and Engineering, UCLA
Synthetic data only | Portfolio project
Notes: I'm walking through a simulated cover-glass yield excursion. All data is synthetic — this is not Apple or supplier confidential data.

## Slide 2
Project Motivation
Why it matters: high-volume cover glass, brittle edge defects
What I saw: CNC edge chipping and chamfer width drift
MQE goal: find high-risk process windows and preventive controls
Synthetic data only | Portfolio project
Notes: Start with the business problem — yield dropped after CNC contouring. My job as MQE is to localize the issue and recommend containment and fixes.

## Slide 3
Manufacturing Problem
AOI yield drop after CNC contouring / chamfering
Edge-initiated defects can feed downstream reliability risk
Phase 1 focus: CNC-related Edge_Chipping
Synthetic data only | Portfolio project
Notes: I'm not trying to solve every defect mode in v1. Edge chipping is the dominant signature, so that's where I focused.

## Slide 4
Synthetic Data Design
What I built: 50,000 synthetic unit-level records
Traceability: machine, fixture, shift, tool life, coolant stability
CTQs, defect mode, defect location, final disposition
Embedded special cause: tool wear × coolant instability
Synthetic data only | Portfolio project
Notes: I designed the dataset to mirror real traceability fields. There's a planted interaction — high tool life plus unstable coolant — so I can show whether analysis finds it without cheating.

## Slide 5
End-to-End Workflow
Generate → validate → Pareto → stratification
SPC → capability → defect-location heatmap
ML risk screening (supporting, not controlling)
JMP interactive review → MQE containment / corrective / preventive actions
Synthetic data only | Portfolio project
Notes: Python runs the reproducible pipeline. JMP is for live filtering and visual confirmation in a cross-functional review.

## Slide 6
Implementation Evidence
What I built: reproducible Python pipeline (`main.py` + `src/`)
50,000-row synthetic dataset in `data/raw/`
JMP import table + project for interactive review
GitHub portfolio with reports, figures, and this deck
This is a working project — not just a slide outline.
50k synthetic raw data
Synthetic data only | Portfolio project

## Slide 7
AI-Assisted Engineering Workflow
I used AI tools to move faster, but I still owned the MQE logic, validation, and conclusions.
Cursor: Python code, debugging, PPT script
Claude Code: Multi-file edits and docs
Python / JMP: Reproducible analytics + review
ChatGPT: planning, MQE storyline, stats review, interview prep | Cursor: implementation | Claude Code: larger refactors | Python + JMP: analytics source of truth + interactive review
AI tools accelerated implementation, but engineering assumptions, validation, leakage control, and MQE interpretation were manually reviewed.
Synthetic data only | Portfolio project
Notes: I used AI to speed up coding and documentation. But I manually checked stats assumptions, ML leakage rules, and every MQE conclusion. Don't oversell AI — it's an accelerator, not the engineer.

## Slide 8
Defect Pareto
What I tested: overall NG defect mix
What the data showed: 3.85% NG rate
Edge_Chipping = 80.95% of NG parts
Why it matters: confirms where to spend root-cause time
Edge chipping dominates — start there before chasing minor modes.
NG defect Pareto (Python)
Synthetic data only | Portfolio project
Notes: First step in any excursion: confirm the defect signature. Three-point-eight-five percent NG, and edge chipping is ~81% of that. That's my Phase 1 scope.

## Slide 9
Traceability & Stratification
What I tested: machine, fixture, shift, tool life, coolant stability
What the data showed: concentration on CNC-04 / CNC-06, FIX-B2 / FIX-C1
Why it matters: narrows from fleet yield to suspect windows
Synthetic data only | Portfolio project
Notes: This is classic traceability work — stratify before you jump to a root cause. A few machines and fixtures light up; that's where I drill deeper.

## Slide 10
Key Finding: Tool Life × Coolant Stability
What I tested: tool-life band × coolant stability
Critical_90_100 + Unstable: 61.52% Edge_Chipping rate
Found through stratification — not assumed upfront
Why it matters: points to tooling + coolant interaction
Edge chipping is not random — it clusters in high tool-life and unstable coolant windows.
Tool life × coolant (JMP review)
Synthetic data only | Portfolio project
Notes: When tool life is critical and coolant is unstable, chipping jumps to 61.5%. I didn't bake this into the headline — stratification rediscovered it.

## Slide 11
SPC Monitoring
What I tested: chamfer width (X-bar/R) and chipping rate (p-chart)
Chamfer is a continuous CTQ; chipping is an attribute rate
I-MR on chipping size kept exploratory (zero-inflated)
Why it matters: separates special cause from normal variation
Use p-chart for chipping rate; control limits are process-derived, not spec limits.
Edge chipping p-chart on CNC-04
Synthetic data only | Portfolio project
Notes: For chipping I prefer the p-chart over I-MR on size because most units are zero.

## Slide 12
Process Capability
What I tested: chamfer width vs spec (LSL 0.25 / USL 0.35 mm)
Cp/Cpk: within-subgroup sigma (Rbar/d2)
Pp/Ppk: overall sigma
Low-risk Cpk ≈ 1.404 | High wear + unstable Cpk ≈ 1.181
High-risk window shifts mean toward USL — capability drops even if spread looks OK.
Chamfer capability by process window
Synthetic data only | Portfolio project
Notes: Capability tells me spec margin, not just pass/fail. Baseline Cpk is ~1.4; the bad window drops to ~1.18 with a mean shift up.

## Slide 13
Defect Location Heatmap
What I tested: where Edge_Chipping shows up on the part
What the data showed: edge location dominates
Corners and feature cutouts are secondary clusters
Why it matters: supports CNC edge / contour root cause
Defects cluster on edges and corners — consistent with CNC contouring, not random handling.
Machine × defect location heatmap
Synthetic data only | Portfolio project
Notes: Location pattern is another sanity check. If chipping were random contamination you'd expect a different map.

## Slide 14
ML Risk Screening
What I tested: can process inputs rank chipping risk before inspection?
No CTQ leakage — process + traceability inputs only
ROC-AUC ~0.95 | PR-AUC ~0.40
Top features: Tool_Life_Pct, Coolant_Pressure_Stability, Coolant_Pressure_bar
ML is a screening aid — rank high-risk windows, not automatic process control.
Random Forest feature importance
Synthetic data only | Portfolio project
Notes: ML supports the same story as stratification.

## Slide 15
JMP Interactive Review Layer
Full 50,000-row dataset imported into JMP
Python = reproducible batch analytics
JMP = interactive filtering, CTQ review, OOC subgroup check
JMP supports live engineering review — Python stays the source of truth for calculations.
Chamfer CTQ distribution
OOC subgroup highlight
Synthetic data only | Portfolio project
Notes: In a real review I'd open the JMP project and filter live. Python generated the numbers; JMP lets the team explore together.

## Slide 16
MQE Recommendations
Containment: hold / sort high-risk lots on CNC-04, CNC-06
Corrective: inspect tooling, coolant system, FIX-B2 / FIX-C1
Preventive: tool-life stop (~75%), coolant interlock, SPC alerts, capability review
MQE action: contain now, fix tooling/coolant/fixtures, then lock in preventive controls.
Synthetic data only | Portfolio project
Notes: Close the loop — containment first so bad material doesn't ship, then corrective on the machines and fixtures that stratified hot, then preventive so it doesn't come back.

## Slide 17
Limitations & Future Work
Synthetic data only — no real AOI images or supplier data
No real DOE or line validation in Phase 1
Future: Streamlit dashboard, DOE simulation, reliability linkage, SHAP
Synthetic data only | Portfolio project
Notes: This demonstrates MQE methodology on simulated data — next step would be real line validation.

## Slide 18
Interview Takeaway
Structured MQE path: signature → traceability → SPC → capability → action
Connects materials / reliability background to manufacturing quality
Python for reproducible analytics; JMP for interactive review
AI-assisted workflow — with manual engineering review
Synthetic data only | Portfolio project
Notes: I confirmed the defect, traced it to tool life and coolant, proved it with SPC and capability, and wrote containment plus preventive controls. All reproducible in Python, reviewable in JMP.

## Slide 19
Thank You
Hexing Yin
GitHub: https://github.com/hexing-yin/mqe-glass-quality-demo
Synthetic data only | Portfolio project